## Slide 1: Recent updates to ANSI MH16.1: perforated rack member design and the Direct Strength Method
Cristopher D. Moen
RunToSolve LLC
Wei-Wen Yu International Specialty Conference on Cold-Formed Steel Structures, Madison, Wisconsin
runtosolve.github.io/ICCFSS2026_MoenRackStandards

## Slide 2: Three editions of MH16.1 in eleven years
ANSI MH16.1 (RMI) is the specification for industrial steel storage racks, referenced by ASCE 7 §15.5.3 and the IBC
Rack uprights are roll-formed, thin, open, and perforated along their full length, so local, distortional, and global buckling interact
The 2021 edition rewrote the member design chapter around elastic buckling analysis; the 2023 edition kept it
This talk: what changed from 2012 to 2023 and where the Direct Strength Method enters

## Slide 3: MH16.1-2012: effective area and the stub-column Q factor
Compression (§4.1.3.1)
• Effective area from the stub-column test:
• Pn = Ae Fn, with Fn from AISI S100 on the gross, unperforated section
• Q = stub column strength / (Fy Anet,min) ≤ 1 (§9.2.2)
Flexure (§4.1.2)
• Round corners for A and I; sharp corners permitted for J, Cw, ro
Distortional (§4.1.3.2)
• One sentence: certain open sections "shall be checked … by testing or rational analysis"
• No equations, no elastic buckling load
Frame stability by the effective length method: down-aisle Kx = 1.7 for unbraced racks, Kt = 0.8

## Slide 4: MH16.1-2021 §8.2.1: perforations become reduced-thickness strips
• Section properties use round corners for everything, including J and Cw (sharp corners are unconservative for torsion)
• Each strip of web or flange that contains perforations is replaced by a solid strip of reduced thickness
• Global and local buckling, kg = 0.6:
• Distortional buckling, kd = 0.8:
• Lnp is the solid length between holes, L the pitch
Source: ANSI MH16.1-2023, Figure 8.2-1, example of perforation strips in a column
• One idealized section feeds the frame model (§7.2.4), the global buckling check, and the finite strip model for Pcrd and Mcrd

## Slide 5: MH16.1-2021/2023 §8.2.2: perforated compression members
Global (8.2-3, 8.2-4)
Py = Fy Anetg; Pcre with K, L from §10.2, §10.3
Local + global (8.2-5, 8.2-6)
Pnlg = Pne if Q ≥ 1 (split out as its own equation in 2023)
Distortional + global (8.2-7, 8.2-8)
for λd = √(Pne / Pcrd) > 0.561, else Pnld = Pne
• Pn = min(Pnlg, Pnld)
• Pcrd: elastic distortional buckling "in accordance with ANSI/AISI S100" on the td section
• Hot-rolled and closed sections: Pnlg only

## Slide 6: Local buckling: still the stub column, in a new form
Local buckling is not a DSM check: there is no Pcrℓ. The perforation and local slenderness effects both come from the stub-column test (§13.2.3, Q = Ptest / (Fy Anetg) ≤ 1, interpolated between tmin and tmax)
The 2021 exponent Q/(1 − Q) makes the local penalty fade as the column becomes globally slender, the same trend as the DSM local–global curve
For a given Q, the new form is less severe at intermediate λc
Both forms with Fn/Fy = Pne/Py on the same area basis. 2012 used Anet,min; 2021 uses Anetg from the strip section.

## Slide 7: Distortional buckling: the Direct Strength Method piece
New in 2021: an explicit distortional check with an elastic buckling load, Pcrd or Mcrd, the DSM ingredient
Same 0.25 / 0.6 coefficients and 0.561 limit as the AISI S100 distortional curve, but anchored at Pne instead of Py
That captures distortional–global interaction, which tests and FE studies on perforated uprights showed (Casafont, Pastor, Roure, Bonada, Peköz)
At λc = 0 the two agree; at intermediate slenderness MH16.1 is lower, and both reach Pne for slender columns
Example with Pcrd = 0.6 Py

## Slide 8: Finite strip analysis on the strip section
Commentary C8: the "most suitable design approach would be to use finite strip analysis combined with the expressions given"
Workflow
  build the round-corner section with td in the perforated strips
  run CUFSM (or any S100 Appendix 2 analysis)
  read Pcrd at the distortional minimum
  the same model with tg gives the global section properties
Basis: tests, shell FE and FSM studies on perforated uprights (Casafont et al., ASCE J. Struct. Eng. 2013, "Design of steel storage rack columns via the Direct Strength Method")
Source: ANSI MH16.1-2023 Commentary, Figure C8.2-5. CUFSM: local minimum at 80 mm (load factor 14.92), distortional at 700 mm (10.63)

## Slide 9: MH16.1-2021/2023 §8.2.3: flexure follows the same pattern
Local + global (8.2-9, 8.2-10)
My = Fy Sfy, with Sfy on the reduced-thickness section
Distortional + global (8.2-11, 8.2-12)
for λd = √(Mne / Mcrd) > 0.673, else Mnld = Mne
• Mn = min(Mnlg, Mnld) for open cold-formed sections bending about the axis of symmetry; hot-rolled and closed sections use Mnlg
• The coefficients match the AISI S100 flexural distortional curve, anchored at Mne like compression
• Mcrd comes from finite strip analysis on the td section, as for Pcrd

## Slide 10: MH16.1-2021: from effective length to direct analysis
§7.2: second-order analysis with notional loads replaces the effective length method
  Ni = 0.004 αYi with the stiffness reduction τb, or 0.005 αYi without; minimum 0.002 αYi
  B2 = 1 / (1 − α PΔ / (Rm H L))
  semi-rigid beam-to-column connections modeled with springs
Down-aisle Kx = 1.0 (§10.2.1)
Member and frame models use the same hole-reduced section properties
Connectors from cyclic tests (§13.5): design moment 0.75 Mmax; stiffness is the secant at 0.8 Mconn,d
New tests: base fixity (§13.6) and frame bracing (§13.7); portal and upright frame tests removed
Seismic aligned to ASCE 7-16; redundancy factor for multiple rows; overstrength design of base plates and anchors (§11.3)
ISO-style reorganization of the whole document

## Slide 11: Recent updates to ANSI MH16.1: perforated rack member design and the Direct Strength Method
Cristopher D. Moen
RunToSolve LLC
Wei-Wen Yu International Specialty Conference on Cold-Formed Steel Structures, Madison, Wisconsin
runtosolve.github.io/ICCFSS2026_MoenRackStandards